## Slide 1: Liquid-Liquid Extraction
Anna Cai, Aaron Casas, Adil Feratovic, Hussein Rezk
04/21/2026

## Slide 2: Introduction & Background
Liquid-Liquid Extraction:
Process where a solute transfers between two immiscible fluids to achieve separation
Driven by differences in equilibrium distribution and solubility
Useful when distillation is inefficient
In this experiment:
Acetic Acid (solute)
White oil (raffinate phase)
Water (solvent/extract phase)

## Slide 3: Principles Behind the Experiment
Phase Equilibrium:
Acetic acid partitions between water and oil based on equilibrium
Where:
: solute conc. in raffinate phase (oil)
: solute conc. in extract phase (water)
: equilibrium constant  Higher K, better extraction
Mass Transfer:
Concentration gradients during mixing in the agitator
Countercurrent Flow:
Phases flow in opposite directions
Maximizes driving force across stages

## Slide 4: Industrial Applications
Petroleum Industry:
Used to remove impurities from fuels
Environmental Industry:
Used to remove pollutants from wastewater
Pharmaceutical Industry:
Used to purify active ingredients

## Slide 5: Experimental Objectives
Operate a 3-stage extraction unit
Extract acetic acid from oil using water
Assess how agitator speed affects efficiency

## Slide 6: Apparatus

## Slide 7: Materials and Supplies
White oil
Glacial acetic acid
Water
Laser tachometer
Buret
Pipette
Erlenmeyer flask
Phenolphthalein indicator
Parafilm
Stir Bar
NaOH

## Slide 8: Experimental Procedure
Perform a titration of a sample from the tank mixture to verify the exact wt% of acetic acid in the tank
  If the tank isn’t at 1 wt% acetic acid, prepare a solution to ensure the tank is at 1 wt% acetic acid
  Mix the acetic acid into the tank by operation of the centrifugal pump in a closed loop
Adjust water flow rate via rotameter to 0.67 GPM and oil flow rate to 0.34 GPM
Turn on the agitators and, using the tachometer, select and calibrate the agitators
Once calibrated, turn the pump back on, close the return valve, and open the valve to the rotameter.
Allow the system to run till extraction occurs and an oil layer forms in each tank, residence time.
Once extraction occurs, note the residence time it took and draw oil and water phase samples from each tank
Titrate each sample against a 0.05 N NaOH and an indicator to determine acetic acid composition

## Slide 9: Results/Discussion
Chart: Acetic Acid Concentration in Raffinate as a Function of Stage Number
| 1 | 2 | 3
RPM 400 | 0.115 | 0.192 | 0.021
RPM 800 | 0.018 | 0.027 | 0.007
RPM 600 | 0.05 | 0.057 | 0.009
Chart: Acetic Acid Concentration in Extract as a Function of Stage Number
| 1 | 2 | 3
RPM 400 | 0.032 | 0.012 | 0.006
RPM 600 | 0.029 | 0.012 | 0.003
RPM 800 | 0.022 | 0.005 | 0.003
Chart: Acetic Acid Concentration in Extract as a Function of Agitator Speed
| 400 | 600 | 800
Stage 1 | 0.032 | 0.029 | 0.022
Stage 2 | 0.012 | 0.012 | 0.005
Stage 3 | 0.006 | 0.003 | 0.003
Chart: Acetic Acid Concentration in Raffinate as a Function of Agitator Speed
| 400 | 600 | 800
Stage 1 | 0.115 | 0.05 | 0.018
Stage 2 | 0.192 | 0.057 | 0.027
Stage 3 | 0.021 | 0.009 | 0.007

## Slide 10
Chart: XA vs YA at 400 RPM
| 0.115 | 0.192 | 2.1000000000000001E-2
 | 0.032 | 0.012 | 0.006
Chart: XA vs YA at 600 RPM
| 0.05 | 5.7000000000000002E-2 | 8.9999999999999993E-3
 | 0.029 | 0.012 | 0.003
Chart: XA vs YA at 800 RPM
| 1.7999999999999999E-2 | 2.7E-2 | 7.0000000000000001E-3
 | 0.022 | 0.005 | 0.003

## Slide 11
Chart: 
| 7.0000000000000007E-2 | 0.06 | 0.05 | 0.03 | 0.02 | 0.03 | 0
XA | 3.27 | 2.39 | 1.79 | 1.19 | 0.9 | 0.57 | 0.26
n | 0.029 | 0.003
Kremser equation
N = Theoretical number of stages
Xf = Feed concentration
Xn = Exit concentration
Ys = Gas – phase Concentration
M = slope

## Slide 12: Conclusion
Raffinate acetic acid concentration decreased across stages, showing effects of countercurrent extraction
Agitator speeds directly affect extraction efficiency; 400 RPM to 800 RPM showed much better performance
A Kremser analysis showed increased efficiency from higher RPM ~0.48 to ~0.61
Higher RPM allows the system to be well mixed, effectively increasing mass transfer and mass transfer area
Found a potential kinetic limitation through mass transfer resistance