## Slide 1: Evaporation
Group #3
Kendall Johnson, Lindsey Meisch
Chemical Engineering Lab I
10/14/2025

## Slide 2: Introduction
The purpose of this lab was to evaluate the performance of a single effect evaporator operating under different vacuum pressures
Determine the effect of pressure on condensate capacity, steam economy and heat transfer behavior

## Slide 3: Introduction
Relate observed data to theoretical principles
Technical Nature
  Evaporation is a heat and mass transfer process
    Used to concentrate a nonvolatile solute in a volatile solvent
  Utilizes vacuum operation to reduce boiling temperature, enhancing heat transfer and energy efficiency

## Slide 4: Theory
Based on heat transfer and phase change from liquid to vapor
Steam condenses on one side of the heat exchanger while the liquid boils on the other
Governing Equations:
  Rate of heat transfer:
  Steam Economy:
  Energy Balance:

## Slide 5: Theory
Assumptions/Limitations
  Negligible heat loss to surroundings
  Steady-state operation and complete condensation of vapor
  Constant physical properties for dilute sugar solution
  Single-effect evaporator limits energy recovery; steam economy < 1

## Slide 6: Theory
Connection to Experiment
  Varying vacuum pressure alters boiling temperature and temperature difference, directly influencing capacity and economy

## Slide 7: Apparatus
Evaporator
Condenser
Vacuum Pump
Distillate/Condensate
Sugar Water Reservoir
Make Up Water Reservoir

## Slide 8: Material & Supplies
Sugar
DI Water
Steam
Cooling water
Thermocouple/Thermocouple Reader
Various Beakers/Graduated Cylinders
Scale
Scoop

## Slide 9: Procedure
A 10 wt% sugar solution was prepared and circulated through the single effect evaporator
Steam was supplied to the heat exchanger and the system was operated under 3 different vacuum pressures
Condensate and distillate volumes were measured at steady-state for each P

## Slide 10: Procedure
Temperatures were recorded at multiple points and the condensate mass flow rate and steam economy were calculated
Pre-Lab Steps
  Ensure vacuum pump and steam traps were functioning properly
  Verify Thermocouple calibration and leak-tight system connections

## Slide 11: Procedure
Critical Lab Tasks
  Maintaining stable vacuum and steam pressures
  Adjusting feed and makeup flow rates to maintain constant liquid level
  Accurate timing and measurement of condensate and distillate collection

## Slide 12: Experimental Challenges
Maintaining consistent vacuum pressure and avoiding air leaks in system
Controlling condensate flow rate and steam valve to avoid over pressurization
Variability in temperature readings due to delayed sensor response
Ensuring proper operation of steam traps and condensate drainage

## Slide 13: Experimental Challenges
Avoid rapid valve adjustments that cause pressure surges
Future Improvements
  Improve insulation to minimize heat loss
  Use real time mass flow sensors for higher accuracy

## Slide 14: Safety
Steam hazards
Vacuum system (ensure components are rated for vacuum use; no cracks/damage)
Hot surfaces
Condensate handling
Spill prevention