## Slide 1: Membrane Air Separation
Group 4
Rishabh S. Patel, Kyle Hankosky, Khoa Nguyen, Alexis Guillen
Chemical Engineering Lab V
11/11/25

## Slide 2: Introduction
The main purpose of this lab is to study gas separation using nonporous polymeric membranes & evaluate how the differences in diffusivity & solubility affect gas transport through this membrane
Membrane Transport
Gas permeation occurs via solution-diffusion process
Governed by Fick’s Law & Henry’s Law
Apparatus & Experimental Setup
Two Prism™ membrane modules containing polysulphone hollow fibres (~2.7m^2 per module)
Can be operated in series or parallel to compare separation efficiency
Compressed air flows through fibre lumens and oxygen-enriched gas permeates into shell side
Data Analysis & Evaluation
Calculate:
  Overall mass-transfer coefficients Selectivity parameters: α, α’, α”
  Recovery and Stage Cut
Analyze effects of pressure and flowrate on transport performance
Plot versus operating pressure

## Slide 3: Theory
Underlying physical principles & Governing equations
Solution-diffusion mechanism
  adsorptiondissolution in polymerdiffusion across membranedesorption
Partial pressure difference across each membrane drives gas
Permeation equation (from Fick & Henry’s Law)
Ideal Selctivity:
Overall mass transfer coefficient
Assumptions & Limitations
Membranes are treated as nonporous, dense and uniformconst. thickness, Z
Steady-State: transient behaviour neglected
Isothermal conditions
Gas phase is ideal
Negligible external mass-transfer resistance
Negligible pressure drop
System treated mainly as a binary mixture
Permeation described only by solution-diffusion
Connection to experiment
Two hollow fibre Prism™ modules are operated either in series or parallel
Measured values:
feed pressure
tube and shell-side flowrates
mole fractions in each stream at ~1atm outlet
Use the measurements to:
Compute fluxes & overall transfer coefficients 
Determine selectivity and experimental separation factors for &
Evaluate recovery and stage cut, to compare performance for series vs. parallel
Directly tests how the equations and assumptions predict real membrane behaviour

## Slide 4: Apparatus
Membrane Separator Modules | Strain-gauge Transducer | 3-Way Directional Valves
Manifold | Oxygen Analyzers | Volumetric flowmeters

## Slide 5: Material & Supplies
Compressed Air Cylinder | Two-stage Pressure Regulator
Hose
Clamp

## Slide 6: Procedure
Preparation
Turn on and calibrate both oxygen analyzers
Plug in the mass flow meters & pressure transducer
Open the high-pressure air cylinder valve and record cylinder pressure (>2000 psig)
Adjust the regulator to desired feed pressure (30-40 psig, for the initial run)
2. Setup Configuration
For Parallel:
  Valve A, left
  Valve B, up
  Valve C, down
  Valve D, up
For Series:
  Valve A, right
  Valve B, up
  Valve C, up
  Valve D, up
3. Operation
Set desired tube-side flowrate using needle valve
Allow readings to stabilize
Record:
  Operating pressure
  Tube and Shell side flowrates
  O2 conc. for each module
  Ambient temp.
4. Data Collection
Perform atleast 15 runs across different pressures
And flowrates
Repeat for both configurations

## Slide 7: Experimental Challenges
Difficulties
Maintaining steady pressure while adjusting needle valve
Recalibrating Oxygen analyzer to ensure accurate readings
Small leaks/valve misalignment which impacted flowrates
Things to watch
Do not leave valves in middle position – causes pressure buildup
Allow analyzers to run for a while before recording data – let readings settle
Ensure each valve position before a run
Recheck flow and pressure after an adjustment
Lessons Learned
Letting readings stabilize before recording can ensure more accurate/consistent data

## Slide 8: Safety
Pressurized gas cylinder – Ensure it stays secured in position, open the valve slowly to prevent pressure shock
Valves – Do not leave valves in middle position, otherwise this can trap pressure and rupture fittings
Leaks – Check fittings for leaks before pressurizing the system