## Slide 1: Evaporation
Group 2
Joshua Laforest, Javier Silva, Ameen Abuzir, and Cesearo Dilosa
Chemical Engineering Lab I
9/16/25

## Slide 2: Introduction
Purpose of lab
Technical nature

## Slide 3: Purpose of lab
The purpose of conducting a evaporation in multiple pressures was to find the impact that would occur to the measuring parameters of this lab:
The influence pressure with "Economy" of running this lab at different pressure readings.
The temperature of the running evaporator at different pressure readings
Pressure influence on the capacity of the evaporator.

## Slide 4: Technical nature of an evaporator at different pressures.
Run a Unit operations Evaporation lab at multiple pressures.
Record and analyze data of heat and mass transfers during operations.
Record the alterations influence of the following operating parameters vacuum level, steam supply, cooling water flow.

## Slide 5: Theory
A separator unit (e.g. evaporator) utilizes heat exchange, to vaporize a volatile solvent (e.g. water) from a nonvolatile solute (e.g. sugar)
The evaporator unit is more efficient if the solution's boiling point is low enough for the hot steam to quickly vaporize it; this is done by using a vacuum system (e.g. vacuum pump)
In our experiment we test if this is true by measuring the capacity (kg H2O per hour) vs efficiency (kg H2O per kg Steam)
Q = UAΔT; this is the design equation for the heat exchanger. This also gives the overall heat added to our solution
We assume that the steam flow rate, solution, and Q is constant

## Slide 6: Apparatus
Separator Vessel- Holds the sugar solution, connected to vacuum pump.
Heat exchanger – Transfers heat from condensing steam to the solution.
Vacuum Pump - Controls system pressure and adjusts boiling point.
Condenser and trap - Condenses steam into Erlenmeyer flask for measurement.
Makeup Tank - Contains DI water for maintaining solution level.
Thermocouples - Measure temperatures at various points in the system.
Pressure Gauge - Indicates system pressure in inches of Hg.

## Slide 7: Material & Supplies
Sugar - The solution that will be evaporated
Deionized Water – Used to help evaporate sugar
Heat gloves - Used to protect hands from burning when handling liquids
Erlenmeyer Flask - Collects steam during the experiment
Steam condensate flask - Contains condensate steam
Thermometer - Measures the temperature and boiling point

## Slide 8: Procedure
A 10 % wt sugar solution was of 2.5-3 L was prepared and loaded into our feed tank
Deionized water was supplied to maintain solution levels
Steam was applied to heat the solution and cooling water to collect condensate
With the vacuum pump on, the pressure was adjusted to reach our desired temperature, keeping the separator valve fixed to maintain steady conditions
After steady state was achieved, condensate and product samples were collected alongside temperature and pressure.

## Slide 9: Safety
Vacuum pressure can cause gas to implode if too high
Water can get on electrical equipment
Flask and vacuum can get hot, wear safety gloves