## Slide 1: Humidification
Group #3
Basil Hashim, Lindsey Meisch, Kendall Johnson
Chemical Engineering Lab I
Date 9/16/25

## Slide 2: Introduction
Make air damp via counter current flows
  Use a wetted column to complete a counter current vapor exchange between compressed dry air and DI water.

## Slide 3: Introduction
Objective
  Determine Y’ and enthalpy
  Calculate heat and mass transfer coefficients
  Use comparison to theoretical data to test how well the models apply to our system

## Slide 4: Theory
Underlying physical principle: Simultaneous heat & mass transfer between air & water
Governing equations:

## Slide 5: Theory
Assumptions/limitations:
  Dilute vapor concentration
  Steady-state operation
  Weak coupling of heat & mass fluxes
Connection to experiment:
  Measure T and humidity at inlet/outlet
  Use psychrometric chart to determine Y’ & enthalpy
  Calculate transfer coefficients
  Compare experimental vs theoretical correlations

## Slide 6: Apparatus
Air Rotameter
Water Rotameter
Wetted Column/Weir
Thermocouples 1-6/Thermocouple reader
Anemometer
Pump
Inlet/outlet

## Slide 7: Material & Supplies
DI Water (approx. ¾ of reservoir)
Funnel/Beaker
Compressed air – Caution
Steam – Caution
Anemometer

## Slide 8: Procedure – Set Up
Set up
  Fill water reservoir with DI water
  Open water flow valve
  Start pump – adjust water flow upwards until column walls are fully wetted, then decrease
  Turn on thermocouple reader
  Adjust air flow as needed

## Slide 9: Procedure – Experiment
Operate the wetted column until steady state for:
  Three temperatures, with three air flows per temperature

## Slide 10: Procedure – Clean Up
Turn off steam if on
Allow water to pump out into drain – do not run the pump dry
Keep compressed air running at approx. 3 SCFD to dry the column.
Turn off thermocouple reader

## Slide 11: Experimental Challenges
Temperature and humidity take a long time to reach steady state – Be Patient
The calculations for this lab are robust – Start Early

## Slide 12: Safety
Water is close to electric components
Compressed air is used (134.7 psia) – rated down
Steam is used (133 deg C) – also rated down
Heat exchanger (used with steam)