## Slide 1: Continuous Distillation
Group #1
Aaron Casas
Anna Cai
Hussein Rezk
Adil Feradovic
Chemical Engineering Lab Il
Date 3-17-26

## Slide 2: Introduction
Purpose of the Lab is to examine continuous distillation of a binary solution (Ethanol, Water) at steady state
Tray efficiency would be analyzed based on feed location.

## Slide 3: Theory
McCabe- Thiele Analysis
  Equilibrium line, operating lines, theoretical stages
  Murphree Efficiency
Distillation Mass Balances
  Overall Mass balance
  Component mass balance
  Equilibrium stage balance
  Energy balance

## Slide 4: Apparatus
Reboiler
Pump
Column
Condenser
Feed tanks
Armfield UOP3CC
Top and bottom product receiver

## Slide 5: Material & Supplies
  Graduated Cylinder
  Stopwatch
  Bucket
  Funnel
  Snap 41 Densitometer
  Sample Flasks
  Parafilm
  DI water
  200 Proof Ethanol
  Cooling Water

## Slide 6: Procedure
Experiment A: Calibration
  Used to get the flowrate of the pump at different turn settings.
Experiment B : Steady State Distillation
  Reflux ratio: 5 to 1
  Reboiler Power: 0.75 kW
  Feed in the middle of the column
  Take 3 samples of tops and bottoms after the column reaches steady state.

## Slide 7: Procedure continued
Experiment C Varying the Feed position
  Disconnect the feed tube, but first temporally turn of the reboiler power.
  Reconnect the tube to the top plate
  Turn reboiler power to .75kW and wait for column to stabilize
  Set reflux to 5:1
  Set feed pump to about 30-35 mL per minute
  After feeding 400 mL take samples from the tops and bottoms
  Take two more samples five minutes apart.

## Slide 8: Experimental Challenges
Making sure the nut is tightened at the feed location
Bottoms flow comes out fast, so turn valve slowly
Collecting tops product can result in alcohol reading difficulties

## Slide 9: Safety
Electrical Hazards
  Use a funnel when pouring the mixtures into their respected location
Mechanical Hazards
  Pump could experience issues
Pressure and Temp Hazards
  Make sure to temp is around 96 degress Celsius
  Wear heat resistant gloves when collecting samples
Chemical Hazards
  200 proof ethanol is used, so create the mixure inside the fume hood, wear chemical gloves, and glasses at all times