## Slide 1: Fluidized Bed
Group #2
Kendall Johnson, Lindsey Meisch, Christian Salinas, Srija Bomma
Chemical Engineering Lab I
2/3/2026

## Slide 2: Introduction
Purpose of lab
  Investigate gas-solid fluidization behavior
  Measure pressure-drop vs superficial gas velocity
Technical nature
  Widely used in catalytic cracking, combustion and gasification, and drying and coating
  Critical for reactor design, pressure drop estimation, scale-up, and process control

## Slide 3: Theory
Fluidization Fundamentals
  Gas flows upward through a particle bed
  At low velocity > packed bed behavior
  At minimum fluidization velocity > drag force = effective bed weight
  Above minimum fluidization velocity > bed expands, pressure drop plateaus

## Slide 4: Theory
Governing Equations
  Ergun equation (packed bed)
  Minimum fluidization condition

## Slide 5: Theory
Assumptions/Limitations
  Resin sphericity = 1
  Uniform size distribution
  Uniform gas distribution
  Steady-state behavior
Connection to experiment
  Pressure-drop plateau at fluidization
  Hysteresis between increasing/decreasing flow
  Agreement with theory within experimental uncertainty

## Slide 6: Apparatus
1: Compressed air inlet gauge
2: Rotameter(s) to control fluid flow through the column
3: Air distributor plate
4: Plexiglass fluidized bed column
5: Manometer

## Slide 7: Material & Supplies
Ion-resin
Sand
Balance
Graduated cylinder
Funnel
Compressed air
Vacuum cleaners
Sieves

## Slide 8: Procedure
Pre-Lab Preparation
  Performed sieve analysis on sand and resin
  Determined average particle diameter
  Measured void fraction using water displacement
Fluidization Experiment
  Loaded bed to 6 and 10 inch heights
  Gradually increase flow
  Record pressure drop, flow rate, and visual bed behavior
  Continued until pressure drop plateaued

## Slide 9: Experimental Challenges
Identifying exact onset of fluidization
Manometer resolution – limited precision
Rotameter accuracy
Bed instability at higher velocities

## Slide 10: Experimental Challenges
Things to watch for
  Small increments for air flow
  Allow system to stabilize
  Read manometer at eye level
  Ensure uniform particle loading and level bed surface
  Avoid sudden valve adjustments

## Slide 11: Experimental Challenges
Lessons learned
  Perform replicate trials earlier for better statistics
  Use lower flow increments around transition region

## Slide 12: Safety
Compressed air
Pressure
Sand/resin slip hazard